KPDY300H 24 Volt DC-DC, 300W ATX with P4 Connector

Top of Form SPECIFICATIONS DC INPUT RATING 24 Vdc 18 Vdc 36 Vdc 22 A(max.) OUTPUT RATING OUTPUT 1 OUTPUT 2 OUTPUT 3 OUTPUT 4 OUTPUT 5 OUTPUT 6 VOLTAGE +5V +3.3V +12V -5V -12V +5V SB MAXIMUM LOAD 35A 14A 12A 1A 2A 1A MINIMUM LOAD 3A 0A 1A 0A 0A 0A PEAK 38A 21A 16A 3A 2A Total combined output of +3.3V and +5V shall not exceed 175W RIPPLE / NOISE 50mVp-p 33mVp-p p 100mVp-p 50mVp-p p 100mVp-p 50mVp-p LINE REGULATION ±1% ±1% ±1% ±1% ±1% ±1% CROSS REGULATION ±5% ±5% ±5% ±2% ±10% ±5% Efficiency 65% at typical load Hold up time 16ms at full load Power good signal 100~500ms Shout Circuit Protection A short circuit on any DC output will cause the power to latch. Over power protection Peak power protected to between 110% to 125% of continuous rated power. Over voltage protection +5V:5.5-6.5V Teamperture range 32°F ~122 °F ( 0~ 50°C) Relative Humidity Operating: 10~90% rh Storage: 5%~90% rh Safety Standards Meets UL 1950, CSA 22.2 No.234, TUV IEC 950, FCC Class B, VDE Class B M.T.B.F. 100k hours at 25°C Dimention (W x H x D ) 150 x 86 x 142 mm/ 5 7/8"x3 3/8"x5 1/2" ORDERING GUIDE Model Description Price KPDY300H 24 Volt DC-DC, 300W ATX with P4 Connecto $195.00 Bottom of Form